CUT TO LENGTH LINE 1.500X3 – 6-HIGH

Manufacturer : HYBRID (the leveller: LDM)

Year when built: completely re-manufactured in 2007

TECHNICAL DATA

- Tensile strength: N/mm² 400

- Yield strength: N/mm² 300

- Strip width: min 400mm max 1.560mm

- Strip thickness: min .6mm max 3.0mm (2.0mm S.S.) *   see note below

- coil weight max: 12 t

- Coil ID: 508mm

- Coil OD max.: 1.700mm

- Sheet length: min 300mm max 4.000mm

- Sheet width: min 300mm max 1.550mm

- Bundle height: max 400mm

- Bundle weight: max 2.500 kg

- Jog speed: 10m / min

- Line operating speed: 0 ÷ 27m / min

- length tolerance (at constant speed): ± .5mm over 2.000mm cut length

*  The thickness range can be extended to .3mm with a second roll set (not included in price)

LINE COMPOSITION

1 – 12 t Coil car, pit type

2 – 12 t Decoiler, with front support

Dynamic braking by hydraulic motor and proportional pressure valve.

3 – Peeler table with pinch rolls

4 – 6-HI leveller, 17-roll / dia. 55mm. Quick roll change system

5 – PVC applicator with feed pinch rolls

7 – Flying shear, 60 cuts/min

8 – Belt conveyor

9 – Exit pinch-rolls

10 – Stacker (4.000mm long), 'no-scratch' type with front & side air kickers

11 – Chain conveyor (4.000mm long)

12 – Hydraulics

13 – Electrics

14 – Perimetric optical+mechanical fencing

N. 1 set of spare work & intermediate rolls

The line is installed and can be demonstrated under power