3107  -  135/12

4-HI PRECISION LEVELLER    1700mm x 3mm

Manufacturer : MARIANI (ITALY)

Year when built: ca. 1980.    Revamped in: 2012

Roll width x diam.: 1790mm x 50mm

Material thickness:  .5 – 3.0 mm (Rm = 420 N/mm2)

No. of work rolls :   17

Backup roll set: 	 7 + 7   /  adjustable through hydraulic jacks, with positioning sensors

Screwdown movement by electric motor, independent for each side

Lubrication system (main gearbox): automatic with electric oil pump

Grease pump on work roll bearings

Tilting movement by electric motor

Gearbox Ratio: 1/10

Speed: 30 m/min with motor speed 2000 rpm  (original motor power: 50 kW-1600 rpm)

Condition: re-manufactured