138/12

4-HIGH PRECISION LEVELLER

1500mm x 2,5mm

“COSMEC”

Maximum material thickness: 2.5mm (Rm = 400 N/mm2)

Minimum  material thickness:   .4mm

Manufacturer: Cosmec (Italy)

Year when built: 1990

Work rolls: 19   - roll dia.: 45mm

Table width = 1.650mm

Back-up roll sets: 7 + 7

Adjustement of each back-up roll set: by pneumatic selector and electric 3-phase motor (380 V – 50 Hz) P=0.75 kW – 1430 rpm .

Positioning sensors on back-up rolls

Screwdown (upper bridge) by 2 separate 3-phase motors, 380 V – 50 Hz    P=1.5 kW-1430 rpm

Entry/exit movement (tilting) by 3-phase motor, 380 V – 50 Hz    P=0.5 kW-1430 rpm

Main gearbox ratio: 1:7.5

Machine operating speed max.: 30m / min

Central lubrication with electric pump, on main gearbox