175/12

1.850mm x 6mm Quick Tool Change Slitting Line

PROCESS MATERIAL SPECS

CR/HR/Galv. Coils

Material thickness min-max: 1-6mm

Coil weight: max 30 t

Coil Width at entry, min-max: 200-1.850mm

Strip Width min. (with the available tooling): 20mm

Coil O.D. at entry, max.: 2.000mm

Slit Coil O.D., max: 1.900mm

Coil I.D. at entry: 500-610-762mm

Coil I.D. at recoiling: 508-610 mm

LINE GENERAL INFO:

Manufacturer: FIMI   /   Full line revamping & additions: SALICO  (2001>2006)

Line direction: Left to Right

Line speed max.: 100m / min

LINE DESCRIPTION:

- Coil Loading Car

hydraulic with no floor pit

- Motorized Decoiler, overhung-drum type

for 500mm Coil I.D., with spacers for 610mm and 762mm I.D.'s

Motorized and braked by D.C. Motor, with hydraulically operated mobile base for centering

Optical-hydraulic Auto. Edge Guide

Hydraulic Snubber Arm with motorized roll (hold-down)

Collapsible Front Support for mandrel

- Coil Threading Station (2001)

Hydraulic Peeler Table

Motorized Pinch Rolls

-Entry Crop Shear (2001)

Guillotine type, hydraulic

- Slitter (2001)

DC motor driven with material entry guide; - shaft diameter: 250mm

Hydraulic clamping of tooling

Auto. Quick Tool Change type with: tooling ejector, swivel head, three-arm turnstile

- Scrap Baler, single-drum type (2001)

Hydraulic

800mm x 800mm

Butt Shear

Semi-auto. scrap lead-in

- Burr Planishing Unit & Scrap Evacuation Table (2001)

- Loop Entry Roll Saddle

Strip Tension Stand (2001)

Roll Saddle at loop exit

Double Separator Arm

Hydraulic Felt Press with pneumatic chambers

Oiler

- Cross Shear & Strip Introduction Unit (2006)

Pinch Rolls

Hydraulic Crop Shear [ # 2 ]

Deflector Roll, coated in oil-proof polyurethane

Telescoping Table

- Recoiler, overhung-drum type (2001)

With D.C. motor drive, hydraulic strip edge clamping

Slit coil I.D.: 508mm with spacers for 610mm

Separator Disc Arm

Hydraulic Ejection Plate with double scraper in bronze

Front Support for mandel

- Coil Off-Loading Car

requiring floor pit

- 4 Arm Turnstile

- Electrics (2001)

with one general Cabinet + three operator pedestals

- Hydraulics & Pneumatics

two hydraulic power packs complete with filters, air/oil heat exchangers, and std. accessories

- Safety Guarding

-Available Tooling

over 100 blades